## Slide 1
AI-Based Proactive Prediction
Of GNSS Signal Degradation
for Autonomous Vehicle Navigation
Team Pilot Project | Beihang University (BUAA)
Supervisor: Dr. Ahmed Wasiu | June 2026
Predicting GNSS degradation before it impacts safety
THE PROMISE
5–30
seconds advance warning
● Predict, not detect
● Multi-horizon: 5 / 15 / 30 s
● Cross-city generalisation
S/N | Name | Student ID
1 | Ojerinde Joel Segun | LS2525253
2 | Mustapha Ibrahim Ishola | LS2525238
3 | Ogunlade Joshua Oluwaseun | LS2525237
4 | Ingeriyinkindi Claudine | LS2525236
5 | Rashid Md Harun Or | LS2525219

## Slide 2
1 · The Problem

## Slide 3
PROBLEM STATEMENT
GNSS is the primary absolute-positioning sensor for autonomous vehicles — yet it fails predictably and frequently in the environments AVs operate in.
1
Urban Canyons
Tall buildings block and reflect satellite signals. Multipath errors corrupt range measurements.
Position jumps of 10–50 m occur silently — the receiver continues reporting a “fix” even as accuracy collapses.
2
Tunnels & Underpasses
Complete signal blockage causes instantaneous position loss.
A reactive system detects failure only after the vehicle has entered the tunnel — too late to plan a safe response or engage backup localisation.
3
Atmospheric Effects
Ionospheric and tropospheric disturbances degrade range accuracy across wide areas.
Effects are gradual and harder to detect — DOP and C/N₀ drift slowly before the solution quality degrades.
Core Problem: All existing monitors (RTKLIB Q-codes, RAIM, ML classifiers) are REACTIVE — autonomous vehicles need advance warning to respond safely.

## Slide 4
PROBLEM STATEMENT
What Early Warning Enables
Horizon
Distance @ 60 km/h
AV Action
+5 s
83 m
Tighten IMU fusion · slow down
+15 s
250 m
Pre-engage dead-reckoning · adjust speed
+30 s
500 m
Re-route away from degradation zone

## Slide 5
2 · Data

## Slide 6
Three sources, one unified schema
149,662 labelled epochs · one unified 3-class schema
3
Cities collected
Beijing · Hong Kong · Tokyo
9+
Receiver types
survey-grade → consumer phone
5
Degradation scenarios A–E
blockage · canyon · partial · open · approaching
1s
Sampling cadence
RINEX + NMEA per epoch
BEIHANG UNIVERSITY
SENTINEL-GNSS · PILOT
DATASET
Notes: Start with the data, because that's where most of the work went. The key idea is on the right of this diagram: three quite different sources all funnel into one unified labelling schema. Beijing is our own field collection on a Septentrio, with the five controlled scenarios A through E. Hong Kong is the public UrbanNav data — that's where the receiver diversity comes from, nine-plus types. And Tokyo we deliberately hold out, so it's a genuine cross-city test. Altogether: just under a hundred and fifty thousand labelled epochs, four cities, nine-plus receivers from survey-grade down to a phone chip, all sampled once a second.

## Slide 7
3 · Method

## Slide 8
Three classes, predicted three steps ahead
CLEAN
WARNING
DEGRADED
30 s of signal in → degradation class out at +5 / +15 / +30 s
BEIHANG UNIVERSITY
SENTINEL-GNSS · PILOT
METHODOLOGY
Notes: Here's the actual problem in one picture. The vertical line is 'now'. To its left is the thirty seconds of signal we observe; to the right is what we predict. The model isn't classifying the present — it's forecasting. As the signal quality drops, it passes from CLEAN into WARNING and eventually DEGRADED, and we read off the predicted class at plus five, plus fifteen, and plus thirty seconds. So in this example it's already flagging a warning at five seconds and a full degradation by thirty — that early amber dot is the whole value proposition.

## Slide 9
From raw signals to model-ready features
37 FEATURES · 7 GROUPS
Position
Signal strength · C/N₀
Satellite count
DOP
Receiver status
Temporal
Atmospheric
1s
RIEX + NMEA per epoch
30 × 37
sliding-window tensor
+5 / 15 / 30s
prediction horizons
BEIHANG UNIVERSITY
SENTINEL-GNSS · PILOT
METHODOLOGY
Notes: Before the model, the feature pipeline. Raw RINEX and NMEA come in once a second and become thirty-seven engineered features in seven groups — position, signal strength, satellite count, DOP, receiver status, temporal patterns, and atmospheric. We stack thirty seconds of those into a thirty-by-thirty-seven tensor with a sliding window, and that tensor is what the model consumes — producing predictions at plus five, fifteen, and thirty seconds. Nothing exotic here on purpose: the features are all standard receiver outputs, which keeps the whole thing reproducible on any of our nine-plus receiver types.

## Slide 10
Inside SENTINEL-GNSS
1.46
M
· trainable parameters · one forward pass
focal loss · γ = 1.0
BEIHANG UNIVERSITY
SENTINEL-GNSS · PILOT
class weights [1 · 2 · 5]
no SMOTE — imbalance at loss level
METHODOLOGY
Notes: Now the model itself. The thirty-by-thirty-seven window is linearly projected and positionally encoded, then runs through two Transformer encoder layers — eight heads, dimension one-twenty-eight — to capture structure across the window, then two BiLSTM layers to model the directional trajectory toward failure, then four output heads: one per horizon plus an auxiliary head. The whole thing is just one-point-four-six million parameters in a single forward pass. Class imbalance is handled in the loss — focal loss with class weights one, two, five — not with resampling.

## Slide 11
4 · Results

## Slide 12
0.821
Macro-F1 +5 s
MCC = 0.773 | CI [0.798–0.840]
0.741
Macro-F1 +15 s
MCC = 0.691 | CI [0.717–0.764]
0.783
Macro-F1 +30 s
MCC = 0.731 | CI [0.758–0.804]
30-second warning with Macro-F1 = 0.783 — nearly as strong as 5-second prediction
Horizon | Acc | Macro-F1 | κ | MCC
+5 s | 0.854 | 0.821 | 0.762 | 0.773
+15 s | 0.789 | 0.741 | 0.667 | 0.691
+30 s | 0.830 | 0.783 | 0.723 | 0.731
MULTI-HORIZON PREDICTION

## Slide 13
Class | Precision | Recall | F1 | Support
CLEAN | 0.868 | 0.993 | 0.927 | 731
WARNING | 0.947 | 0.718 | 0.817 | 746
DEGRADED | 0.623 | 0.847 | 0.718 | 209
DEGRADED Recall = 0.847
Catches 85% of impending signal failures — 5 s ahead
WARNING Precision = 0.947
When the model says WARNING, it is right 95% of the time
CLEAN F1 = 0.927
Rarely triggers false alarms on healthy signal
PER-CLASS PERFORMANCE @ +5 S

## Slide 14
Method | +5s F1 | +15s F1 | +30s F1 | MCC
MajorityClass | 0.202 | 0.072 | 0.072 | 0.000
CNR Threshold | 0.074 | 0.072 | 0.072 | 0.000
RandomForest (SMOTE) | 0.909 | 0.887 | 0.877 | 0.915
XGBoost (SMOTE) | 0.910 | 0.898 | 0.879 | 0.915
RandomForest (no-SMOTE) | 0.910 | 0.891 | 0.896 | 0.916
XGBoost (no-SMOTE) | 0.919 | 0.896 | 0.879 | 0.926
Transformer-only | 0.767 | 0.763 | 0.701 | 0.725
LSTM-only | 0.767 | 0.751 | 0.781 | 0.702
SENTINEL-GNSS (ours) | 0.821 | 0.741 | 0.783 | 0.773
⚠️
In-domain: XGBoost 0.919 outperforms DL 0.821
✅
Cross-city: DL retains DEGRADED F1 — trees collapse (see Novelty)
🚀
One model, one pass — 10.5× faster than 3 tree models
COMPARISON TO ALL BASELINES

## Slide 15
Model | +5s F1 | +15s F1 | +30s F1
Transformer-only | 0.767 | 0.763 | 0.701
LSTM-only | 0.767 | 0.751 | 0.781
SENTINEL-GNSS | 0.821 | 0.741 | 0.783
Full model beats both ablations at +5s and +30s
BiLSTM alone is strong for longer horizons (+30s)
Transformer-only struggles at +30s — sequence matters there
ABLATION STUDY — WHAT EACH COMPONENT ADDS

## Slide 16
CROSS-CITY GENERALISATION — TOKYO

## Slide 17
KEY RESULT
XGBoost
0.822 → 0.148
DEGRADED F1 in-domain → Tokyo
−82% collapse
CROSS-CITY GENERALISATION — TOKYO SHINJUKU
0.718 → 0.753
SENTINEL-GNSS
DEGRADED F1 in-domain → Tokyo
+5% improvement
Model | Beihang/Beijing | Tokyo | Tokyo DEGRADED F1
DL + XGBoost ENSEMBLE | 0.911 | 0.892 | 0.896
SENTINEL-GNSS (DL) | 0.822 | 0.649 | 0.753
XGBoost | 0.919 | 0.821 | 0.784
RandomForest | 0.926 | 0.618 | 0.148

## Slide 18
10.52×
faster than 3 separate tree models
0.039 ms / sample vs 0.409 ms / sample
SENTINEL-GNSS
0.039 ms
All 3 horizons in one forward pass
3 × Tree models
0.409 ms
One model per horizon
17.8 MB
Model size
1,456,652 parameters
< 0.04%
CPU budget
10 Hz vehicle compute
INFERENCE SPEED & EFFICIENCY

## Slide 19
Transformer Attention — DEGRADED sample
Feature Saliency (gradient) @ +5 s
INTERPRETABILITY — ATTENTION & FEATURE SALIENCY
Notes: Model attends strongly to the most recent timesteps before failure
Top saliency features: C/N₀, PDOP, num_satellites, fix quality
Tree models cannot provide this mechanistic transparency

## Slide 20
State | ECE
Raw (T = 1.0) | 0.114
After scaling (T = 0.4023) | 0.068
Improvement | −40%
Temperature scaling converts raw logits to more reliable probability estimates — enabling P(DEGRADED) to serve as a risk score for the adaptive EKF.
PROBABILITY CALIBRATION — TEMPERATURE SCALING

## Slide 21
Horizon | Distance @ 60 km/h | Action Window
+5 s | 83 m | Lane-change preparation, pre-buffer switch
+15 s | 250 m | Alternative route segment selection
+30 s | 500 m | INS / HD-Map localisation handover
❌ Reactive (RTKLIB / RAIM / prior ML)
Reports: Signal failed
Vehicle already in degraded zone — zero prep time
✅ Proactive (SENTINEL-GNSS)
Reports: Signal will fail in T seconds
Vehicle gets an actionable preparation window
N1 — PROACTIVE PREDICTION

## Slide 22
5.5 · EKF: From Prediction to Position

## Slide 23
• Cross-city: DL+XGBoost ensemble is best (Macro-F1 0.892, DEGRADED 0.896).
• Inference: 0.045 ms/sample on GPU — ~9.5x faster than three separate tree models.
• One 17.8 MB checkpoint serves all three horizons; real-time at 10 Hz.
• Calibration: temperature scaling cuts ECE 40% (0.114 -> 0.069); not yet <0.05 (future work).
• Persistence baseline scores 0.91 at +5s -> the model's value is transitions + longer horizons.
EFFICIENCY, ENSEMBLE & CALIBRATION

## Slide 24
Raw GNSS trajectory vs adaptive EKF on real Beihang field NMEA; P(DEGRADED) predictions.
REAL DATA EKF CASE STUDY

## Slide 25
E1
Temporal Shuffle Test
Shuffling timesteps drops F1 by ~3.2% — temporal order contributes, but the dominant advantage is representation.
E2
Temporal Feature Ablation (RF)
Removing temporal features reduces RF Macro-F1 by ~4.8%; confirms temporal features matter for trees too.
E3
Bootstrap 95% CI (1000 iter)
DEGRADED F1 = 0.718 [0.671, 0.762] — all claims backed by confidence intervals.
E4
Inference Latency (Tesla T4)
SENTINEL-GNSS: 0.039 ms vs 3 tree models: 0.409 ms — 10.52× speedup.
E5
SMOTE Distribution Analysis
SMOTE hurts XGBoost (Δ=−0.0095); focal loss + class weights suffice for the network.
E6
Cross-City Tokyo Shinjuku
XGBoost DEGRADED F1: 0.822 → 0.148 (−82%). SENTINEL-GNSS: 0.718 → 0.753 (+5%). KEY RESULT.
E7
Calibration ECE
ECE 0.114 → 0.068 after T-scaling. ⚠️ Re-run in progress with T=0.4023 hard-set.
VALIDATION

## Slide 26
5 · Novelty & Validation

## Slide 27
1
Reactive → Proactive Predictor
First system to predict GNSS degradation 5 s, 15 s, 30 s ahead — Liu et al. (2023) only classifies t+0
2
Cross-City Generalisation
Beijing → Tokyo: DEGRADED F1 = 0.75 (ours) vs. 0.15 (Random Forest) — unseen city, zero retraining
3
Unified Multi-Horizon Model
One forward pass, three prediction heads — 10.5× faster than three separate traditional models
4
Open Multi-City Benchmark
149,662 labelled epochs · Beijing, Hong Kong, Tokyo, Oxford, Ann Arbor · 9+ receiver types
5
Hardware-Aware Design
Explicit receiver_tier feature bridges Septentrio survey-grade → consumer smartphone, no retraining
10.5× faster · one pass · three horizons
DEGRADED F1: 0.75 (ours) vs 0.15 (RF) on unseen Tokyo
5 s
≈ 83 m
SENSOR TIGHTENING
Fuse IMU/LiDAR · tighten tracking loops before canyon entry
15 s
≈ 250 m
SENSOR HANDOFF
Shift EKF authority to dead-reckoning before signal loss
30 s
≈ 500 m
ROUTE REPLANNING
Full lead time to commit to an alternative route
NOVELTIES

## Slide 28
0.8206
Macro-F1 (+5 s)
95% CI [0.798, 0.840]
85%
DEGRADED Recall
safety-critical class
0.75
DEGRADED F1 — Tokyo
vs. RF = 0.15 out-of-domain
±5 cm
Ground-truth accuracy
LiDAR SLAM · NCLT dataset
Session-Based Split — No Data Leakage
▸ Whole drives assigned to train / val / test — never individual seconds
▸ Tokyo Shinjuku (31,236 windows) fully held out as cross-city test (E6)
▸ StandardScaler + SMOTE fitted on training set only · Seed = 42
Physically Verified Labels
▸ NCLT: labels from |GPS − LiDAR SLAM| — actual positioning error, ±5 cm
▸ Septentrio thresholds 35 / 25 dBHz confirmed by hardware signal charts
▸ NMEA no-fix epochs (quality = 0) correctly captured as DEGRADED
Honest Comparison with Classical Baselines
▸ XGBoost Macro-F1 = 0.919 vs. ours 0.821 in-domain — disclosed openly
▸ Cross-city: RF DEGRADED F1 collapses to 0.15 · ours holds at 0.75
▸ One model, 10.5× faster, calibrated probabilities (ECE < 0.05)
Uncertainty & Ablation Evidence
▸ Bootstrap 95% CIs on all metrics: DEGRADED F1 [0.647, 0.789]
▸ Permutation test (E5): temporal order adds ~3 pp — gain is representation transfer
▸ Ablation: full model > Transformer-only > LSTM-only on DEGRADED F1
VALIDATION

## Slide 29
6 · Roadmap & Deliverables

## Slide 30
Paper A
Proactive Multi-Horizon GNSS Degradation Prediction
GPS Solutions (Springer, Q1) · Target: Post-ION GNSS+ 2026
🔄 Drafting
Paper B
From Prediction to Position: Adaptive EKF
IEEE T-ITS / Journal of Navigation (Q1) · Target: After Paper A submission
⏳ Outlined
Conference
Cross-City Transfer — Short Paper
ION GNSS+ 2026 · Target: Check deadline
⏳ Outlined
PUBLICATION ROADMAP
Literature Review
Title: Evolution of Intelligent GNSS Signal Degradation Prediction Techniques for Autonomous Vehicle Navigation
⏳ Outlined
Paper C

## Slide 31
1-month total · 2 concurrent coursework · Critical path: data collection (Wk 1) → model training (Wk 3) · Target: IEEE T-ITS
Week 1 · Days 1–7
Setup & Data Extraction
All software installed · Room 3058 visit · GitHub repo created
All
ROSBAG extraction + RTKLIB running on supervisor vehicle & drone datasets
Joshua
Scenarios A & D collected (5 reps each) · RTKLIB processed
Claudine, Joshua
Week 2 · Days 8–14
Full Collection & Features
Scenarios B, C, E collected · Feature CSVs generated · Labelling complete
Claudine, Joshua
All baseline models trained & results recorded (RF, LSTM, threshold, RAIM)
Harun
Literature review drafted (30 papers) · UrbanNav & RobotCar processed
Harun, Claudine
Week 3 · Days 15–21
Model Training & System Build
Transformer-LSTM trained · First test-set results · Ablation studies done
Joel
Generalisation tests on UrbanNav & RobotCar · KAIST on arrival
Joel, Claudine
Dynamic EKF in simulation · Dashboard all 5 panels with data playback
Mustapha
Week 4 · Days 22–28
Integration, Demo & Paper
Live campus test: cart + receiver + dashboard · Screen capture video
All
Paper 1 first draft written · Each member fills their sections
Joel leads
Full team review · Presentation rehearsed · Submission-ready draft
All
⚠ Risk: Scenarios A & D (Day 5–7) are the critical path — all model work depends on them. KAIST delay does not block; UrbanNav + RobotCar alone prove cross-geography generalisation.
PROJECT TIMELINE — 4-WEEK COMPRESSED PLAN

## Slide 32
Thank you
SENTINEL-GNSS — predicting GNSS degradation before it happens
Team Pilot Project · Beihang University
github.com/Jorshuare/AI-Based-Prediction-for-GNSS-Signal-Degradation