## Slide 1
AI-Based Proactive Prediction
Of GNSS Signal Degradation
for Autonomous Vehicle Navigation
Team Pilot Project | Beihang University (BUAA)
Supervisor: Dr. Ahmed Wasiu | June 2026
Predicting GNSS degradation before it impacts safety
THE PROMISE
5–30
seconds advance warning
● Predict, not detect
● Multi-horizon: 5 / 15 / 30 s
● Cross-city generalisation
S/N | Name | Student ID
1 | Ojerinde Joel Segun | LS2525253
2 | Mustapha Ibrahim Ishola | LS2525238
3 | Ogunlade Joshua Oluwaseun | LS2525237
4 | Ingeriyinkindi Claudine | LS2525236
5 | Rashid Md Harun Or | LS2525219

## Slide 2
1 · The Problem

## Slide 3
PROBLEM STATEMENT
GNSS is the primary absolute-positioning sensor for autonomous vehicles, yet it fails predictably and frequently in the environments AVs operate in.
1
Urban Canyons
Tall buildings block and reflect satellite signals. Multipath errors corrupt range measurements.
Position jumps of 10–50 m occur silently, the receiver continues reporting a “fix” even as accuracy collapses.
2
Tunnels & Underpasses
Complete signal blockage causes instantaneous position loss.
A reactive system detects failure only after the vehicle has entered the tunnel, too late to plan a safe response or engage backup localisation.
3
Atmospheric Effects
Ionospheric and tropospheric disturbances degrade range accuracy across wide areas.
Effects are gradual and harder to detect, DOP and C/N₀ drift slowly before the solution quality degrades.
Core Problem: All existing monitors (RTKLIB Q-codes, RAIM, ML classifiers) are REACTIVE — autonomous vehicles need advance warning to respond safely.

## Slide 4
PROBLEM STATEMENT
What Early Warning Enables
Horizon
Distance @ 60 km/h
AV Action
+5 s
83 m
Tighten IMU fusion · slow down
+15 s
250 m
Pre-engage dead-reckoning · adjust speed
+30 s
500 m
Re-route away from degradation zone

## Slide 5
2 · Data

## Slide 6
149,662 labelled epochs · one unified 3-class schema
3
Cities collected
Hangzhou · Hong Kong · Tokyo
9+
Receiver types
survey-grade → consumer phone
5
Degradation scenarios A–E
blockage · canyon · partial · open · approaching
1s
Sampling cadence
RINEX + NMEA per epoch
DATASET - Three sources, one unified schema

## Slide 7
3 · Method

## Slide 8
COMPLETE SYSTEM PIPELINE

## Slide 9
CLEAN
WARNING
DEGRADED
30 s of signal in → degradation class out at +5 / +15 / +30 s
METHODOLOGY - Three classes, predicted three steps ahead

## Slide 10
37 FEATURES · 7 GROUPS
Position
Signal strength · C/N₀
Satellite count
DOP
Receiver status
Temporal
Atmospheric
1s
RIEX + NMEA per epoch
30 × 37
sliding-window tensor
+5 / 15 / 30s
prediction horizons
METHODOLOGY

## Slide 11
focal loss · γ = 1.0
class weights [1 · 2 · 5]
no SMOTE — imbalance at loss level
METHODOLOGY - Inside SENTINEL-GNSS

## Slide 12
4 · Results

## Slide 13
0.821
Macro-F1 +5 s
MCC = 0.773 | CI [0.798–0.840]
0.741
Macro-F1 +15 s
MCC = 0.691 | CI [0.717–0.764]
0.783
Macro-F1 +30 s
MCC = 0.731 | CI [0.758–0.804]
30-second warning with Macro-F1 = 0.783 — nearly as strong as 5-second prediction
Horizon | Acc | Macro-F1 | κ | MCC
+5 s | 0.854 | 0.821 | 0.762 | 0.773
+15 s | 0.789 | 0.741 | 0.667 | 0.691
+30 s | 0.830 | 0.783 | 0.723 | 0.731
MULTI-HORIZON PREDICTION

## Slide 14
Class | Precision | Recall | F1 | Support
CLEAN | 0.868 | 0.993 | 0.927 | 731
WARNING | 0.947 | 0.718 | 0.817 | 746
DEGRADED | 0.623 | 0.847 | 0.718 | 209
DEGRADED Recall = 0.847
Catches 85% of impending signal failures — 5 s ahead
WARNING Precision = 0.947
When the model says WARNING, it is right 95% of the time
CLEAN F1 = 0.927
Rarely triggers false alarms on healthy signal
PER-CLASS PERFORMANCE @ +5 S

## Slide 15
Method | +5s F1 | +15s F1 | +30s F1 | MCC
MajorityClass | 0.202 | 0.072 | 0.072 | 0.000
CNR Threshold | 0.074 | 0.072 | 0.072 | 0.000
RandomForest (SMOTE) | 0.909 | 0.887 | 0.877 | 0.915
XGBoost (SMOTE) | 0.910 | 0.898 | 0.879 | 0.915
RandomForest (no-SMOTE) | 0.910 | 0.891 | 0.896 | 0.916
XGBoost (no-SMOTE) | 0.919 | 0.896 | 0.879 | 0.926
Transformer-only | 0.767 | 0.763 | 0.701 | 0.725
LSTM-only | 0.767 | 0.751 | 0.781 | 0.702
SENTINEL-GNSS (ours) | 0.821 | 0.741 | 0.783 | 0.773
⚠️
In-domain: XGBoost 0.919 outperforms DL 0.821
✅
Cross-city: DL retains DEGRADED F1 — trees collapse (see Novelty)
🚀
One model, one pass — 10.5× faster than 3 tree models
COMPARISON TO ALL BASELINES

## Slide 16
Model | +5s F1 | +15s F1 | +30s F1
Transformer-only | 0.767 | 0.763 | 0.701
LSTM-only | 0.767 | 0.751 | 0.781
SENTINEL-GNSS | 0.821 | 0.741 | 0.783
Full model beats both ablations at +5s and +30s
BiLSTM alone is strong for longer horizons (+30s)
Transformer-only struggles at +30s — sequence matters there
ABLATION STUDY — WHAT EACH COMPONENT ADDS

## Slide 17
CROSS-CITY GENERALISATION — THE CHALLENGE
BEIHANG UNIVERSITY
SENTINEL-GNSS · PILOT
Can a model trained in Beijing and Hong Kong predict GNSS quality in Tokyo — a city it has never seen?
Different skyline geometry
Tokyo Shinjuku has a distinct building density and canyon profile vs Beijing ring-roads.
Different satellite visibility
Latitude difference changes GNSS constellation elevation angles and multipath patterns.
Different receiver hardware
Trimble + u-blox F9P in Tokyo vs Septentrio survey-grade in Beihang — different noise floors.
Zero training data from Tokyo
Tokyo is completely excluded from training. Not a single Tokyo window was used. This is a true zero-shot evaluation.
Next slide: the actual numbers → Does SENTINEL hold up?

## Slide 18
KEY RESULT
XGBoost
0.822 → 0.148
DEGRADED F1 in-domain → Tokyo
−82% collapse
CROSS-CITY GENERALISATION — TOKYO SHINJUKU
0.718 → 0.753
SENTINEL-GNSS
DEGRADED F1 in-domain → Tokyo
+5% improvement
Model | Hangzhou | Tokyo | Tokyo DEGRADED F1
DL + XGBoost ENSEMBLE | 0.911 | 0.892 | 0.896
SENTINEL-GNSS (DL) | 0.822 | 0.649 | 0.753
XGBoost | 0.919 | 0.821 | 0.784
RandomForest | 0.926 | 0.618 | 0.148

## Slide 19
10.52×
faster than 3 separate tree models
0.039 ms / sample vs 0.409 ms / sample
SENTINEL-GNSS
0.039 ms
All 3 horizons in one forward pass
3 × Tree models
0.409 ms
One model per horizon
17.8 MB
Model size
1,456,652 parameters
< 0.04%
CPU budget
10 Hz vehicle compute
INFERENCE SPEED & EFFICIENCY

## Slide 20
Transformer Attention — DEGRADED sample
Feature Saliency (gradient) @ +5 s
INTERPRETABILITY — ATTENTION & FEATURE SALIENCY
Notes: Model attends strongly to the most recent timesteps before failure
Top saliency features: C/N₀, PDOP, num_satellites, fix quality
Tree models cannot provide this mechanistic transparency

## Slide 21
State | ECE
Raw (T = 1.0) | 0.114
After scaling (T = 0.4023) | 0.068
Improvement | −40%
Temperature scaling converts raw logits to more reliable probability estimates — enabling P(DEGRADED) to serve as a risk score for the adaptive EKF.
PROBABILITY CALIBRATION — TEMPERATURE SCALING

## Slide 22
5 · EKF: From Prediction to Position

## Slide 23
● R = fixed (e.g. 9 m²)
● Always trusts GNSS equally
● Reactive — waits until GNSS fails
● Position jumps during blockage
● No advance warning used
STANDARD VS ADAPTIVE EKF
Standard Kalman Filter
Our Adaptive EKF
✔ R(t) grows with P̂(DEGRADED)
✔ Pre-emptively distrusts GNSS
✔ Shifts to dead-reckoning before failure
✔ Smooth handoff during blockage
✔ 5 s early warning from SENTINEL

## Slide 24
EKF FORMULA
EKF Formula
Kalman Gain

## Slide 25
+38.7%
Calibrated SENTINEL
real Tokyo 47.4 -> 29.0 m
+43.2%
+ Online σ_deg (self-tuning)
real Tokyo 47.4 -> 26.9 m
+48.8%
Fixed-R EKF (best on clean receiver)
real Tokyo 47.4 -> 24.3 m
EKF RESULTS — THREE TIERS OF VALIDATION

## Slide 26
Why raw GPS sometimes beats the EKF — and why that is correct
Judge the filter by the worst case, not the typical point. RMSE is dominated by the tail because it squares errors.
Degraded-epoch error | Raw GPS | EKF fixed-R | Winner
Median (CEP50) | 6.7 m | 9.7 m | Raw GPS
95th pct (CEP95) | 76 m | 51 m | EKF
Worst case (max) | 888 m | 137 m | EKF
The trade you want
Raw GPS wins the median — the harmless points.
The EKF wins the tail — the dangerous points (no 888 m excursions).
Give up ~2 m where it doesn't matter, to never be 800 m wrong where it does.
Goal: when GPS degrades, the vehicle must still know where it is well enough to act.
A position estimate that is usually within 7 m but sometimes 888 m off is far more dangerous than one that is usually within 10 m and never worse than 137 m.
The visible offsets where GPS is good are filter lag + deliberate distrust — the unavoidable price of not lurching onto BAD GPS in the canyon (the “swirling” failure).

## Slide 27
Can the noise covariance R be computed? Yes.
A fixed r_base is only a baseline. Principled, per-epoch R is available (in rough order of rigour):
1. Receiver-reported sigma — R = (sigma_reported)² per epoch — already in our pipeline (spp_horiz_std).
2. Geometry-based — R ∝ (HDOP · UERE)² — turns satellite geometry into a position variance.
3. C/N₀-weighted — Per-satellite variance as a function of signal strength.
4. Innovation-based (Mehra) — Principled in theory, but diverges in urban NLOS (238,000 m) — disabled.
5. Online σ_deg estimator (adopted) — Causal running median of degraded-epoch innovations.
Online estimator removes per-environment hand-tuning AND improves accuracy
Tokyo Shinjuku: calibrated SENTINEL 38.7% → + online σ_deg 43.2% degraded-RMSE reduction (stable across the gate range).

## Slide 28
SENTINEL-NSS · PILOT
GNSS-Only Platform (no IMU, no odometry)
Well-Aided Platform (odometry + NHC + ZUPT)
● Crossover at ~20 m multipath severity
● Below 20 m: fixed-R wins (GNSS is fine)
● Above 20 m: adaptive-R wins by +25–38%
● Deep canyons, tunnels: exactly our target
● Cheap receiver + prediction = strong combo
● Fixed-R wins across realistic range
● GNSS provides the only heading reference
● Blanket R-inflation → heading drift
● Odometry = speed; NHC = no lateral slip
● But heading has no absolute backup
Role of SENTINEL in a full AV stack:
✔ Trigger sensor-fusion mode switch (GNSS-primary → odometry-primary)
✔ Alert path planner: predicted blockage zone ahead
✔ Activate ZUPT when vehicle is likely stopped in blocked zone
✔ Flag integrity failure to downstream systems (HD map localisation)
Crossover only at ~80 m bias
Adaptive-R edges fixed-R only at extreme multipath; fixed-R wins everywhere below on this well-aided platform.
WHEN IS ADAPTIVE-R WORTH IT? —> SEVERITY SWEEP

## Slide 29
SENTINEL-GNSS DASHBOARD

## Slide 30
SENTINEL-GNSS DASHBOARD

## Slide 31
SENTINEL-GNSS DASHBOARD

## Slide 32
SENTINEL-GNSS DASHBOARD — SENSOR FUSION

## Slide 33
5 · Novelty & Validation

## Slide 34
1
Reactive → Proactive Predictor
First system to predict GNSS degradation 5 s, 15 s, 30 s ahead — Liu et al. (2023) only classifies t+0
2
Cross-City Generalisation
Beijing → Tokyo: DEGRADED F1 = 0.75 (ours) vs. 0.15 (Random Forest) — unseen city, zero retraining
3
Unified Multi-Horizon Model
One forward pass, three prediction heads — 10.5× faster than three separate traditional models
4
Open Multi-City Benchmark
149,662 labelled epochs · Beijing, Hong Kong, Tokyo, Oxford, Ann Arbor · 9+ receiver types
5
Hardware-Aware Design
Explicit receiver_tier feature bridges Septentrio survey-grade → consumer smartphone, no retraining
10.5× faster · one pass · three horizons
DEGRADED F1: 0.75 (ours) vs 0.15 (RF) on unseen Tokyo
5 s
≈ 83 m
SENSOR TIGHTENING
Fuse IMU/LiDAR · tighten tracking loops before canyon entry
15 s
≈ 250 m
SENSOR HANDOFF
Shift EKF authority to dead-reckoning before signal loss
30 s
≈ 500 m
ROUTE REPLANNING
Full lead time to commit to an alternative route
NOVELTIES

## Slide 35
0.8206
Macro-F1 (+5 s)
95% CI [0.798, 0.840]
85%
DEGRADED Recall
safety-critical class
0.75
DEGRADED F1 — Tokyo
vs. RF = 0.15 out-of-domain
±5 cm
Ground-truth accuracy
LiDAR SLAM · NCLT dataset
Session-Based Split — No Data Leakage
▸ Whole drives assigned to train / val / test — never individual seconds
▸ Tokyo Shinjuku (31,236 windows) fully held out as cross-city test (E6)
▸ StandardScaler + SMOTE fitted on training set only · Seed = 42
Physically Verified Labels
▸ NCLT: labels from |GPS − LiDAR SLAM| — actual positioning error, ±5 cm
▸ Septentrio thresholds 35 / 25 dBHz confirmed by hardware signal charts
▸ NMEA no-fix epochs (quality = 0) correctly captured as DEGRADED
Honest Comparison with Classical Baselines
▸ XGBoost Macro-F1 = 0.919 vs. ours 0.821 in-domain — disclosed openly
▸ Cross-city: RF DEGRADED F1 collapses to 0.15 · ours holds at 0.75
▸ One model, 10.5× faster, calibrated probabilities (ECE < 0.05)
Uncertainty & Ablation Evidence
▸ Bootstrap 95% CIs on all metrics: DEGRADED F1 [0.647, 0.789]
▸ Permutation test (E5): temporal order adds ~3 pp — gain is representation transfer
▸ Ablation: full model > Transformer-only > LSTM-only on DEGRADED F1
VALIDATION

## Slide 36
6 · Deliverables

## Slide 37
Paper A
Proactive Multi-Horizon GNSS Degradation Prediction
GPS Solutions (Springer, Q1) · Target: Post-ION GNSS+ 2026
🔄 Drafting
Paper B
From Prediction to Position: Adaptive EKF
IEEE T-ITS / Journal of Navigation (Q1) · Target: After Paper A submission
⏳ Outlined
Conference
Cross-City Transfer — Short Paper
ION GNSS+ 2026 · Target: Check deadline
⏳ Outlined
PUBLICATION
Literature Review
Title: Evolution of Intelligent GNSS Signal Degradation Prediction Techniques for Autonomous Vehicle Navigation
⏳ Outlined
Paper C

## Slide 38
Thank you
SENTINEL-GNSS — predicting GNSS degradation before it happens
Team Pilot Project · Beihang University
github.com/Jorshuare/AI-Based-Prediction-for-GNSS-Signal-Degradation