## Slide 1
AI-Based Proactive Prediction
Of GNSS Signal Degradation
for Autonomous Vehicle Navigation
Team Pilot Project | Beihang University (BUAA)
Supervisor: Dr. Ahmed Wasiu | June 2026
Predicting GNSS degradation before it impacts safety
S/N | Name | Student ID
1 | Ojerinde Joel Segun | LS2525253
2 | Mustapha Ibrahim Ishola | LS2525238
3 | Ogunlade Joshua Oluwaseun | LS2525237
4 | Ingeriyinkindi Claudine | LS2525236
5 | Rashid Md Harun Or | LS2525219

## Slide 2
Table Of Contents
01
The Problem
a
02
Data
03
Methodology
04
Results
a
05
EKF: From Prediction to Position
05
Novelty and Validation
06
Deliverables
a
07
References

## Slide 3
1 · The Problem

## Slide 4
PROBLEM STATEMENT
GNSS is the primary absolute-positioning sensor for autonomous vehicles, yet it fails predictably and frequently in the environments AVs operate in.
1
Urban Canyons
Tall buildings block and reflect satellite signals. Multipath errors corrupt range measurements.
Position jumps of 10-50 m occur silently, the receiver continues reporting a “fix” even as accuracy collapses.
2
Tunnels & Underpasses
Complete signal blockage causes instantaneous position loss.
A reactive system detects failure only after the vehicle has entered the tunnel, too late to plan a safe response or engage backup localization.
3
Atmospheric Effects
Ionospheric and tropospheric disturbances degrade range accuracy across wide areas.
Effects are gradual and harder to detect, DOP and C/N₀ drift slowly before the solution quality degrades.
Core Problem: All existing monitors (RTKLIB Q-codes, RAIM, ML classifiers) are REACTIVE - autonomous vehicles need advance warning to respond safely.

## Slide 5
PROBLEM STATEMENT

## Slide 6
2 · Data

## Slide 7
149,662 labelled epochs · one unified 3-class schema
3
Cities collected
Hangzhou · Hong Kong · Tokyo
9+
Receiver types
survey-grade → consumer phone
5
Degradation scenarios A-E
blockage · canyon · partial · open · approaching
1s
Sampling cadence
RINEX + NMEA per epoch
DATASET - Three sources, one unified schema

## Slide 8
3 · Method

## Slide 9
COMPLETE SYSTEM PIPELINE
Position
Signal strength · C/N₀
Satellite count
DOP
Receiver status
Temporal
Atmospheric
1s
RINEX + NMEA per epoch
30 × 34
sliding-window tensor
+5 / 15 / 30s
prediction horizons

## Slide 10
CLEAN
WARNING
DEGRADED
30 s of signal in → degradation class out at +5 / +15 / +30 s
METHODOLOGY - Three classes, predicted three steps ahead

## Slide 11
focal loss · γ = 1.0
class weights [1 · 2 · 5]
no SMOTE - imbalance at loss level
METHODOLOGY - Inside SENTINEL-GNSS

## Slide 12
4 · Results

## Slide 13
0.821
Macro-F1 +5 s
MCC = 0.773 | CI [0.798-0.840]
0.741
Macro-F1 +15 s
MCC = 0.691 | CI [0.717-0.764]
0.783
Macro-F1 +30 s
MCC = 0.731 | CI [0.758-0.804]
30-second warning with Macro-F1 = 0.783 - nearly as strong as 5-second prediction
Horizon | Acc | Macro-F1 | κ | MCC
+5 s | 0.854 | 0.821 | 0.762 | 0.773
+15 s | 0.789 | 0.741 | 0.667 | 0.691
+30 s | 0.830 | 0.783 | 0.723 | 0.731
MULTI-HORIZON PREDICTION
Prediction Horizon

## Slide 14
Class | Precision | Recall | F1 | Support
CLEAN | 0.868 | 0.993 | 0.927 | 731
WARNING | 0.947 | 0.718 | 0.817 | 746
DEGRADED | 0.623 | 0.847 | 0.718 | 209
DEGRADED Recall = 0.847
Catches 85% of impending signal failures - 5 s ahead
WARNING Precision = 0.947
When the model says WARNING, it is right 95% of the time
CLEAN F1 = 0.927
Rarely triggers false alarms on healthy signal
PER-CLASS PERFORMANCE @ +5S

## Slide 15
Method | +5s F1 | +15s F1 | +30s F1 | MCC
MajorityClass | 0.202 | 0.072 | 0.072 | 0.000
CNR Threshold | 0.074 | 0.072 | 0.072 | 0.000
RandomForest (SMOTE) | 0.909 | 0.887 | 0.877 | 0.915
XGBoost (SMOTE) | 0.910 | 0.898 | 0.879 | 0.915
RandomForest (no-SMOTE) | 0.910 | 0.891 | 0.896 | 0.916
XGBoost (no-SMOTE) | 0.919 | 0.896 | 0.879 | 0.926
Transformer-only | 0.767 | 0.763 | 0.701 | 0.725
LSTM-only | 0.767 | 0.751 | 0.781 | 0.702
SENTINEL-GNSS | 0.821 | 0.741 | 0.783 | 0.773
In-domain: XGBoost 0.919 outperforms DL 0.821
Cross-city: DL retains DEGRADED F1 trees collapse
One model, one pass; 10.5× faster than 3 tree models
COMPARISON TO ALL BASELINES

## Slide 16
Model | +5s F1 | +15s F1 | +30s F1
Transformer-only | 0.767 | 0.763 | 0.701
LSTM-only | 0.767 | 0.751 | 0.781
SENTINEL-GNSS | 0.821 | 0.741 | 0.783
Full model beats both ablations at +5s and +30s
LSTM alone is strong for longer horizons (+30s)
Transformer-only struggles at +30s; sequence matters there
ABLATION STUDY - WHAT EACH COMPONENT ADDS

## Slide 17
CROSS-CITY GENERALISATION - THE CHALLENGE
Can a model trained in Beijing and Hong Kong predict GNSS quality in Tokyo - a city it has never seen?
Different skyline geometry
Tokyo Shinjuku has a distinct building density and canyon profile versus Beijing ring-roads.
Different satellite visibility
Latitude difference shifts GNSS constellation elevation angles and multipath patterns.
Different receiver hardware
Trimble + u-blox F9P in Tokyo versus Septentrio survey-grade in Beihang - different noise floors.
Zero training data from Tokyo
Tokyo is excluded from training entirely. Not one Tokyo window was used - a true zero-shot test.

## Slide 18
KEY RESULT
XGBoost
0.822 → 0.148
DEGRADED F1 in-domain → Tokyo
−82% collapse
CROSS-CITY GENERALISATION - TOKYO SHINJUKU
0.718 → 0.753
SENTINEL-GNSS
DEGRADED F1 in-domain → Tokyo
+5% improvement
Model | Hangzhou | Tokyo | Tokyo DEGRADED F1
DL + XGBoost ENSEMBLE | 0.911 | 0.892 | 0.896
SENTINEL-GNSS (DL) | 0.822 | 0.649 | 0.753
XGBoost | 0.919 | 0.821 | 0.784
RandomForest | 0.926 | 0.618 | 0.148

## Slide 19
10.52×
faster than 3 separate tree models
0.039 ms / sample vs 0.409 ms / sample
SENTINEL-GNSS
0.039 ms
All 3 horizons in one forward pass
3 × Tree models
0.409 ms
One model per horizon
17.8 MB
Model size
1,456,652 parameters
< 0.04%
CPU budget
10 Hz vehicle compute
INFERENCE SPEED & EFFICIENCY

## Slide 20
5 · EKF: From Prediction to Position

## Slide 21
● R = fixed (e.g. 9 m²)
● Always trusts GNSS equally
● Reactive - waits until GNSS fails
● Position jumps during blockage
● No advance warning used
STANDARD VS ADAPTIVE EKF
Standard Kalman Filter
Adaptive EKF
✔ R(t) grows with P̂(DEGRADED)
✔ Pre-emptively distrusts GNSS
✔ Shifts to dead-reckoning before failure
✔ Smooth handoff during blockage
✔ 5 s early warning from SENTINEL

## Slide 22
EKF FORMULA
EKF Formula

## Slide 23
EKF FORMULA: Kalman Gain

## Slide 24
Degraded-Segment RMSE gain vs. Raw GPS
Trimble Shinjuku: EKF fixed-R wins (24.3 m). u-blox: Huber EKF wins. Odaiba: Student-t PF wins.
No single method dominates - SENTINEL adaptive-R pairs best with clean GPS, the most common case.
EKF MULTI-ENVIRONMENT RESULTS

## Slide 25
WHEN IS ADAPTIVE-R WORTH IT? - > SEVERITY SWEEP
When adaptive-R helps
GNSS-only platform: adaptive-R wins above ~80 m multipath - deep canyons and tunnels, exactly the target regime.
Well-aided platform (odometry + NHC + ZUPT): fixed-R wins; the crossover appears only near ~80 m bias.
Role in the AV stack
Trigger the fusion mode switch (GNSS-primary to odometry-primary), alert the path planner to a predicted blockage zone, and activate ZUPT in blocked zones.

## Slide 26
SENTINEL-GNSS DASHBOARD

## Slide 27
SENTINEL-GNSS DASHBOARD - SENSOR FUSION

## Slide 28
5 · Novelty & Validation

## Slide 29
1
Reactive → Proactive Predictor
First system to predict GNSS degradation 5 s, 15 s, 30 s ahead - Liu et al. (2023) only classifies t+0
2
Cross-City Generalisation
Hangzhou → Tokyo: DEGRADED F1 = 0.75 (ours) vs. 0.15 (Random Forest) - unseen city, zero retraining
3
Unified Multi-Horizon Model
One forward pass, three prediction heads - 10.5× faster than three separate traditional models
4
Open Multi-City Benchmark
149,662 labelled epochs · Beijing, Hong Kong, Tokyo, Oxford, Ann Arbor · 9+ receiver types
5
Hardware-Aware Design
Explicit receiver_tier feature bridges Septentrio survey-grade → consumer smartphone, no retraining
10.5× faster · one pass · three horizons
DEGRADED F1: 0.75 (ours) vs 0.15 (RF) on unseen Tokyo
5 s
≈ 83 m
SENSOR TIGHTENING
Fuse IMU/LiDAR · tighten tracking loops before canyon entry
15 s
≈ 250 m
SENSOR HANDOFF
Shift EKF authority to dead-reckoning before signal loss
30 s
≈ 500 m
ROUTE REPLANNING
Full lead time to commit to an alternative route
NOVELTIES

## Slide 30
0.8206
Macro-F1 (+5 s)
95% CI [0.798, 0.840]
85%
DEGRADED Recall
safety-critical class
0.75
DEGRADED F1 - Tokyo
vs. RF = 0.15 out-of-domain
±5 cm
Ground-truth accuracy
RTK ground truth accuracy (Trimble)
Session-Based Split - No Data Leakage
▸ Whole drives assigned to train / val / test - never individual seconds
▸ Tokyo Shinjuku (31,236 windows) fully held out as cross-city test (E6)
▸ StandardScaler + SMOTE fitted on training set only · Seed = 42
Physically Verified Labels
▸ NCLT: labels from |GPS − LiDAR SLAM| - actual positioning error, ±5 cm
▸ Septentrio thresholds 35 / 25 dBHz confirmed by hardware signal charts
▸ NMEA no-fix epochs (quality = 0) correctly captured as DEGRADED
Honest Comparison with Classical Baselines
▸ XGBoost Macro-F1 = 0.919 vs. ours 0.821 in-domain - disclosed openly
▸ Cross-city: RF DEGRADED F1 collapses to 0.15 · ours holds at 0.75
▸ One model, 10.5× faster, calibrated probabilities (ECE < 0.05)
Uncertainty & Ablation Evidence
▸ Bootstrap 95% CIs on all metrics: DEGRADED F1 [0.647, 0.789]
▸ Permutation test (E5): temporal order adds ~3 pp - gain is representation transfer
▸ Ablation: full model > Transformer-only > LSTM-only on DEGRADED F1
VALIDATION

## Slide 31
6 · Deliverables

## Slide 32
Paper A
Proactive Multi-Horizon GNSS Degradation Prediction
GPS Solutions (Springer, Q1) · Target: Post-ION GNSS+ 2026
🔄 Drafting
Paper B
From Prediction to Position: Adaptive EKF
IEEE T-ITS / Journal of Navigation (Q1) · Target: After Paper A submission
⏳ Outlined
Conference
Cross-City Transfer - Short Paper
ION GNSS+ 2026 · Target: Check deadline
⏳ Outlined
PUBLICATION
Literature Review
Title: Evolution of Intelligent GNSS Signal Degradation Prediction Techniques for Autonomous Vehicle Navigation
⏳ Outlined
Paper C

## Slide 33
Thank you
SENTINEL-GNSS - predicting GNSS degradation before it happens
Team Pilot Project · Beihang University
github.com/Jorshuare/AI-Based-Prediction-for-GNSS-Signal-Degradation

## Slide 34
REFERENCES